## Slide 1: Part 1: Using STELLOPT/REGCOIL and to find a better winding surface for QHS46 Part 2: Discrete coils, free-boundary VMEC MHD solutions and Boozer spectra
John C. Schmitt
A. Bader, M. Landreman, S. Lazerson, E. Paul
Internal Draft Slides, April 2018

## Slide 2: STELLOPT can now manipulate the set of Fourier coefficients that describe the coil winding surface
Winding surface is specified by a set of Fourier coefficients in toroidal space
  Coordinate system
    Superimpose Cartesian (X, Y, Z) and spherical (R, , Z)
  The surface (2D manifold) is defined by the locus of point given by
Stellarator symmetry is enforced for now
  With stellarator symmetry, many modes must be 0: All: All: , and some (m,n) combinations
  The ability to allow non-stellarator symmetry has been implemented, but not tested
STELLOPT varies the coefficients and improves the quality of Bnorm on the target surface
  Initial guess: A winding surface with a uniform separation (See previous presentations)
  Optimal winding surface: For QHS46, the initial trend is to make the winding surface:
    Vertically elongated
    Closer to the plasma, radially

## Slide 3: STELLOPT finds a better solutions (smaller residual error, reduced on the target plasma surface) when manipulating the Fourier coefficients. An improvement by one order of magnitude compared to the uniform winding surface.
Initial guess was a winding surface with uniform separation, KRMS= 2.82e6 A/m
1618 total harmonics were allowed to be varied
1618 identical targets of
Behavior exhibits a dependence on L-M optimizer run parameters of FACTOR / EPSFCN
Time limit reached
  Cases b, c, f, g, i
“algorithm estimates that the relative error between x and the solution is at most xtol”
  Cases a, d, e, h

## Slide 4: The next 21 slides show the evolution of the new ‘optimal’ solution during case 1b with FACTOR/EPSFCN = 25 / 1e-5
This is the case shown in red ‘+’ symbols, see arrows
The first slide will explain what is being shown in each subplot
There are 21 set of plots, one for each new solution

## Slide 5: As an example, the first step (but don’t dwell on it)
X, Y, Z axis units are meters
Upper Left: The original winding surface (in black) and the new winding surface (orange) are superimposed on the same axes. This allows a simple ‘binary’ eye inspection to see the gross features of the surfaces
Upper Right: Planar slices of the winding surface at
Lower left and right: The distance (in cm) from the new surface to the original surface, multiplied by the sign of the change in the vertical (Z) –direction
Original target |B| on target LCFS also shown for reference
  This is not a ‘self-consistent’ |B|

## Slide 6: Iterative solution #2, The first step

## Slide 7: Iterative solution #3

## Slide 8: Iterative solution #4

## Slide 9: Iterative solution #5

## Slide 10: Iterative solution #6

## Slide 11: Iterative solution #7

## Slide 12: Iterative solution #8

## Slide 13: Iterative solution #9: A new rate of descent begins now; Surface will become narrower and taller.

## Slide 14: Iterative solution #10

## Slide 15: Iterative solution #11

## Slide 16: Iterative solution #12

## Slide 17: Iterative solution #13

## Slide 18: Iterative solution #14

## Slide 19: Iterative solution # 15

## Slide 20: Iterative solution # 16: Descent slows down from here on to the end

## Slide 21: Iterative solution #17

## Slide 22: Iterative solution #18

## Slide 23: Iterative solution #19

## Slide 24: Iterative solution #20

## Slide 25: Iterative solution #21

## Slide 26: Iterative solution #22: (24x32 cpu-hour time limit)
The solution after the last iteration is teller and narrower than the starting position
Recall: The starting position was a ‘uniform distance’ away from the plasma boundary

## Slide 27: The optimizer runs that demonstrated the most rapid descent A) look a little different, B) are still evolving, and C) terminated because the solver was in a local minimum (I think)
The surfaces of the two branches that descend more rapidly, but are truncated, look a little different
blue +’s (upper left)
red squares (lower left)
The red square descent path has one extra step – see lower right plots
The solver got stuck in a local minimum?
  “algorithm estimates that the relative error between x and the solution is at most xtol”

## Slide 28: The optimizer branch that descends more slowly looks vaguely like the ‘best’ case: Taller, narrower.
*

## Slide 29: Helical Stripes: The runs that descend very slowly has very corrugated surfaces.

## Slide 30: Conclusions, Part 1
It works, but the routine may not be optimized, robust, nor guaranteed to be globally relevant. Still, it’s a tool that we can tinker with, so why not try?
  Mod. L-M routine documentation is sparse; Some ‘improvements’ are self-documented; Intent/side effects of some code choices are not explained.
  Outline of routine to be done.
Perhaps a Quasi-Newton (or QN-like) step may be more robust
  When the following are true:
    A step along a variable (or several variables) shows an improvement (along a vector/direction)
    and repeated steps (2 or more) along this direction (or set of directions) continue to show improvements
  Then:
    Hypothesis: The local space is well-described by the finite-step forward-difference calculation of the 1st derivative and an estimate of the 2nd derivative is reasonable (along the search vector)
    These steps or directions should be rewarded/trusted and the search and/or step distance along this direction may be accelerated – via a Taylor expansion including 1st and 2nd derivatives
  Additional ‘history’ of the function evaluations needs to be maintained

## Slide 31: Part 2: Discrete coils and the subsequent Boozer spectrum

## Slide 32: Coils, MHD equilibrium and Boozer spectrum for two different winding surfaces: ‘Uniform distance’ and ‘Fourier/Optimized’
Cutting coils, calculating the vacuum VMEC MHD solution and Boozer spectrum
Generate coilsets for two different winding surfaces
  The 1st winding surface is ‘uniformly displaced’ from the plasma
    Shown in a previous Group Meeting: March 23, 2018 @ https://wistell.engr.wisc.edu/?page_id=156
  The 2nd winding surface is the one found by STELLOPT with Fourier Series variations
    shown in detail on slides 4-26 on this presentation
  Coilsets explored consist of a discrete number of unique coils
    Uniform winding surface: 4, 5, 6 (Surfaces are not great)
    Fourier/Optimized winding surface: 3, 4, 5, 6 (VMEC converged with even only 3 coils/FP)
VMEC(+post) are run for each of the cases
  Free-boundary VMEC (using the coils via an ‘mgrid’)
  Boozer spectrum (xbooz_xform)
FOR NOW, I only show the case with 6 coils
Other cases are interesting, but the ‘best Boozer spectrum’ results to date have been found with 6 coils per field period

## Slide 33: Slide labels
Slide 34
  Mod B on LCFS for: QHS46 and Coil set with {4, 5, or 6} coils on uniformly displaced surface
  Lots of tight twists, closely-fitted high-curvature sections. Not great results
Slide 35
  Mod B on LCFS for: QHS46 and with 6 Coils / field period on the Fourier/Optimized surface
  Also see the interactive Matlab figure
Slide 36: Different views of the coils
Slide 37:|B| near LCFS from Boozer spectrum for QHS46 (target) and with 6 coils / field period
Slide 38-39: Boozer spectrum comparison QHS46 (target) and with 6 coils / field period
Slide 40: Boozer spectrum comparison QHS46 (target) and with 3, 4, and 5 coils / field period

## Slide 34: 4, 5, or 6 Coils / field period Uniform winding surface, 2.82e6 A/m

## Slide 35: 6 Coils / field period Fourier/Optimized winding surface 2.82e6 A/m on winding surface; 1.5 MA in each coil
Also see the interactive matlab figure:

## Slide 36: 6 Coils / field period Fourier/Optimized winding surface

## Slide 37: 6 Coils / field period Fourier/Optimized winding surface |B| near target surface looks qualitatively good
|B| as calculated from Boozer spectrum
  Left: QHS46 (the target) Right: 6 coils on optimal winding surface

## Slide 38: 6 Coils / field period Fourier/Optimized winding surface Boozer spectrum is matched well
QHS46 Target
6-coil on Opt. W.S.
QHS46 Target
6-coil on Opt. W.S.

## Slide 39: 6 Coils / field period Fourier/Optimized winding surface Top 5 Boozer modes (after B00, B41) are well-matched
QHS46 Target
6-coil on Opt. W.S.
Small coil ripple (see inset figure)
  Target has extremely small residual B48,0 mode
  Discrete coilset has small ripple term at edge: B48,0 0.001

## Slide 40
QHS46 Target
3-coil on Opt. W.S.
4-coil on Opt. W.S.
5-coil on Opt. W.S.

## Slide 41: Conclusions, Part 2
Coilset with 6 unique coils produces good results
  Good |B|
  Good Boozer spectrum
  Small coil ripple
Original hypothesis is still not proven
  The inverse distance between coils scales with
  This was performed for a single value of .
    With this surface, scan regularization parameter, and see how behaves
    Try other values of and compare coil sets
  Characterize the distance between coils as a function of
    Minimum, Mean
    Problem sections
    # coils / surface

## Slide 42: STELLOPT finds better winding surfaces when manipulating the Fourier coefficients. Discrete coils have favorable features: Good spacing and desired magnetic spectrum.
It works; It is probably not optimized.
It’s a tool that we can tinker with
Desire to make the routine more robust
  Can a Quasi-Newton-like step achieve better results?
  Are local minima and shallow plateaus (un)avoidable?
Discrete coils generate a spectrum that matches the target very well
Does the inverse distance between coils scale with ?
  Probably have a better chance of answering this with an adjustable W.S. than with a uniformly separated W.S.
Repeat this exercise with A) QAS and B) Different number of field periods
  Any interesting features, benefits or challenges?

## Slide 43: Extra

## Slide 44: Background about REGCOIL1,2, 1
‘Regularized NESCOIL’ (REGCOIL) finds the current potential, , on a winding surface such that the following function is minimized:
Normal component of B on the plasma surface:
Current density on the winding surface:
Inverse distance between coils (proxy):
Regularization parameter:
  Larger (more regularization) leads to less complicated current potential contours (‘less harmonic content’), but increases
1 M. Landreman, Nuclear Fusion 57, 046003 (2017).
2 https://github.com/landreman/regcoil
(Check Normalization)